## Slide 1: Drone Phenology Monitoring
Gaurav Rajput
Parth Thakur

## Slide 2: Objective
Align tree crowns from two orthomosaic-derived crowns (OM3 → OM4), resolve missing crowns, and identify geometric mismatches.

## Slide 3: Workflow Steps
CRS Unification
Reprojected both OM3 and OM4 crowns to match the CRS of the raster image sit_om4.tif.
Affine Alignment (OM3 → OM4)
Matched crowns via nearest neighbor centroid search (within 10 meters).
Computed rigid affine transform (scale + rotation + translation).
Applied it to OM3 → significantly improved spatial match.
IoU improved from ~30% → ~72% Transformed OM3 saved as: crowns3_aligned.gpkg

## Slide 4: Crown Completion Logic
A).
Handle Completely Missing Crowns (IoU = 0)
OM3-only crowns (not found in OM4) were copied to OM4 (origin = "from_om3")
OM4-only crowns were similarly added to OM3 (origin = "from_om4")
Inverse affine transform applied to OM4 crowns when transferring to OM3 → Ensures alignment correctness after full transformation

## Slide 5: Crown Completion Logic
B.)
Partial Mismatches (IoU < 63%) —> A−B / B−A
Computed crown difference geometries:
  OM3 crown − OM4 crown → added to OM4 as "om3_diff"
  OM4 crown − OM3 crown → added to OM3 as "om4_diff"
These are visualized as yellow and purple-outlined polygons in the plot Highlights incomplete overlaps or shape shifts between datasets
A-B
B-A

## Slide 6: Summary of Results
Aspect | Outcome
Initial Average IoU | ~30%
Post-Alignment Best IoU | ~72.99%
IoU Threshold for Diff Detection | 63% (relative scale)
Crown Transfers (IoU = 0) | Applied (w/ inverse affine)
Difference Masks (A−B / B−A) | Visualized and Saved

## Slide 7: Impact
Developed an automated framework to:
Align and merge crown datasets
Address missing & misaligned regions
Visually identify crown mismatches

## Slide 8
Thank You